AXI4 Manager Interface
BM component
(SafeTI)
AXI4 Manager
interface
AXI4 Subordinate
interface
AXI4 Network

---
AXI4 Protocol features
- Every transaction is executed through a burst, where many beats transfers
 are executed until the completion of the burst.
- The subordinates allocate 4kB of memory (4096 address spaces). This
 sets the 4kB boundary rule where any burst must not surpass the 4kB
 address space, since every burst is specific to a subordinate.
- The protocol features 5 channels (group of busses); AW, AR, W, R and B.
- The read and write data busses are extensible from 8 upto 1024 bits in
 power of two’s steps. The width of the data bus fixes what addresses
 each byte lane can access. For instance, 64 and 128 bus width:
7/F	6/E	5/D	4/C	3/B	2/A	1/9	0/8
Addresses ended in 0xXX &
F	E	D	C	B	A	9	8	7	6	5	4	3	2	1	0

---
AXI4 Bus use
Handshake	Beats	Response
Use AX* channel:	Read transactions:	Read transactions:
  M -> S	M -> S, R channel:	S -> M, R channel:
> Burst mode.	> Ready data.	> Burst response.
> Starting address.	S -> M, R signals:
> Size mode.	> Read data.	Write transactions:
> Burst length.	> Valid data.	S -> M, B channel:
> Valid control.	> Last beat.	> Beat response.
- ID.	Write transactions:
- Memory region.	M -> S, W channel:
- Lock.	> Write data.	S: Subordinate.
- Cache.	> Valid data.	M: Manager.
- Protected.	> Last beat.
- QOL.	- Write strobe.	*: X is W for write
  S -> M	S -> W, W channel:	and R for read
> Control ready.	> Ready data.	transactions.

---
AXI4 Manager interface structure for Handshake
BM
Component
AXI4
BRAM
Subordinate
I/O Registration
4kB address
boundary check
Decide size mode
Decide length +
Starting address
I/O Registration
I/O Registration
4kB address
boundary check
Decide size mode
Decide length +
Starting address
I/O Registration
RD request
RD grant
WR request
WR grant
AR valid
AR ready
AW valid
AW ready

---
AXI4 Manager interface structure for data transfer
BM
Component
AXI4
BRAM
Subordinate
I/O Registration
BM mask
I/O Registration
I/O Registration
I/O Registration
RD valid
WR data
WR ready
R ready
R valid
W valid
W ready
FIFO
Shifter
AXI strobe
FIFO
Shifter
AXI mask

---
AXI4 Transaction example
BM read transaction request:
Starting address = 0x0FFB
Total size transfer = 23 bytes
(codification) = 0x16
Let’s suppose a BM data bus width of 32 bits
(dbits) and an AXI data bus width of 128 bits
(AXI4_DATA_WIDTH).

---
AXI4 Transaction example
Let’s suppose a BM data bus width of 32 bits
(dbits) and an AXI data bus width of 128 bits
(AXI4_DATA_WIDTH).
0x0FFB + 23 data bytes – 1 = 0x1011 <- Last read address to BM transfer.
    ^---------------------------------------^- Acces to two different subordinates is required.

---
AXI4 Transaction example
Let’s suppose a BM data bus width of 32 bits
(dbits) and an AXI data bus width of 128 bits
(AXI4_DATA_WIDTH).
0x0FFB + 23 data bytes – 1 = 0x1011 <- Last read address to BM transfer.
    ^---------------------------------------^- Acces to two different subordinates is required.
First burst:
0x0FFF – 0x0FFB = 5 data bytes -> Size mode is 8 bytes/beat.
Only one beat is required with a starting address of 0x0FF0.
Second burst:
23 data bytes – 5 data bytes = 18 data bytes -> Size mode is 16 bytes/beat.
(Size mode limited by AXI4_DATA_WIDTH)
      Two beats are required with a starting address of 0x1000.

---
AXI4 Transaction example
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01

---
AXI4 Transaction example
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01

---
AXI4 Transaction example
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01

---
AXI4 Transaction example
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01

---
AXI4 Transaction example
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01

---
AXI4 Transaction example
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01

---
AXI4_DATA_WIDTH
dbits
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF0
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01
127	96	64	32	0 31	0
     : AXI read data, but it’s unrequested by BM.	: BM requested data from first, second and third beats.
(*): Skipped time slots. Represented to better conceptualize the state of the different FIFO regs with the dbits slot.

---
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01
127	96	64	32	0 31	0
t(0)
t(1)
(*)
AXI4_DATA_WIDTH
dbits
fifo(0)
valid
done
BM control
0 0
1 0
     : AXI read data, but it’s unrequested by BM.	: BM requested data from first, second and third beats.
(*): Skipped time slots. Represented to better conceptualize the state of the different FIFO regs with the dbits slot.

---
Since the 4kB boundary space is
expected to be surpassed by the
request, two AXI bursts are generated.
First AXI burst:
Starting address = 0x0FF8
Size mode = 8 bytes = 011’b
Burst length = 1 beat = 0x00
Second AXI burst:
Starting address = 0x1000
Size mode = 16 bytes = 100’b
Burst length = 2 beats = 0x01
127	96	64	32	0 31	0
t(0)
t(1)
(*)
(*)
t(2)
t(3)
t(4)
t(5)
(*)
(*)
t(6)
AXI4_DATA_WIDTH
dbits
fifo(0)
fifo(1)
fifo(2)
valid
done
BM control
0 0
1 0
1 0
1 0
1 0
1 0
1 1
     : AXI read data, but it’s unrequested by BM.	: BM requested data from first, second and third beats.
(*): Skipped time slots. Represented to better conceptualize the state of the different FIFO regs with the dbits slot.

---
127	96	64	32	0 31	0
t(0)
t(1)
(*)
(*)
t(2)
t(3)
t(4)
t(5)
(*)
(*)
t(6)
AXI4_DATA_WIDTH
dbits
fifo(0)
fifo(1)
fifo(2)
valid
done
BM control
0 0
1 0
1 0
1 0
1 0
1 0
1 1
     : AXI read data, but it’s unrequested by BM.	: BM requested data from first, second and third beats.
(*): Skipped time slots. Represented to better conceptualize the state of the different FIFO regs with the dbits slot.

---
AXI4 Narrow transfer example
Source: “Figure A3-14 Aligned and unaligned transfers on a 64-bit bus”, page A3-58, from ARM IHI 0022H.c
    "AMBA AXI and ACE Protocol Specification”.

---
AXI4 Narrow transfer example on faulty subordinate
Hand-	1st beat	2nd beat	3rd beat	4th beat
shake

---
Conclusions
- Started the design of the interface executing narrow bursts always. But,
 due to the characteristics of the subordinate used for debugging, the
 interface has been modified to only execute narrow bursts if they occur in
 different AXI4_DATA_WIDTH addresses (more efficient).
- The modifications have made the interface to be incapable of managing
  multiple narrow bursts that occur on the same AXI4_DATA_WIDTH slot.
  However, it also has given a step to simplify the interface logic, that it
  could be simplified even further. This would be by setting an AXI size mode
  adjusted to AXI4_DATA_WIDTH, saving resources and even a clock cycle.
- At the moment, the AXI4 Manager interface only executes incremental
 bursts.